An approach for Fusarium diseased corn kernels recognition using linear discrete models

P. Daskalov, V. Mancheva, Ts. Draganova, R. Tsonev

Abstract: New approach to identify infected with Fusarium pink maize seeds through the spectral features in the near infrared region is proposed in the paper. It is based on analysis of coefficients of linear parametric models of discrete type Autoregresion (AR). Seeds identification criterion is based on the limit value of АLV between the class healthy and class infected seeds. The maximum distance between the two classes - ΔA for the 10th order of AR-model is used to determine the limit value. The recognition accuracy achieved 100% for a variety XM87/136 and for varieties 26a Knezha 436 and Rouse 424 it’s range is from 97.5 to 98.75%.

Key words : Near infrared spectral characteristics, linear discrete model of the Autoregression type, Corn Kernels, Fusarium Disease

Introduction

Maize diseases are widely spread in all the regions where it is grown and they are one of the most important factors with negative influence on the maize yields. The infectious diseases caused by viruses, fungi and bacteria are significant for the crops, as well as for the production. The pink ear rot is characterised by the appearance of separate smaller or bigger areas of kernels all over the corncob with white to pink fungal deposits. Most often, the deposits are on the lower part of the maize shucks, at places damaged by insects or when the kernel endosperm is cracked in its upper or lower part. The cause for the pink ear rot is the disease Fusarium Moniliforme [5].

When evaluating the quality of agricultural products, not only should certain indicators be controlled, but also the diseased products should be separated from the healthy ones. The quality identification methods could be divided into subjective (organoleptic) and objective (technical, mechanical) methods. The flaws of the subjective methods are mainly the lack of identical perceptions of the different subjects and the instability of perception over time due to tiredness, absent-mindedness, age and other differences. The objective quality identification methods are of physical and chemical nature mainly and they could be defined into the following groups: mechanical, physical, chemical, electromagnetic [1]. The methods based on the measuring of electromagnetic radiation (electromagnetic fields, roentgen radiations, radiations in the visible (VIS), ultraviolet (UV) and infrared (IR) areas, laser radiations, etc.) meet the modern requirements of remote and non-destructive quality determination [1]. Of all of the above methods, the optical ones (UV, VIS, IR) achieve high quality measurement accuracy and correspond very well to the technology conditions and requirements [1].

Delwiche [6] identifies wheat kernels infected with mould through spectroscopy of a reflection in the near infrared region. High classification accuracy of 95 per cent is achieved and it is established that the best classification model uses a combination of the grain mass and the difference of the reflection coefficients of the wave lengths – 1182 and 1242 nm. It is established that the most informative wavelengths for a wheat grains sorting machine (for separation of healthy grains and Fusariosis infected grains) are achieved through a linear discriminant analysis. 95 per cent accuracy of separation is achieved with wavelength of 500 and 550 nm for the visible region, and 97 per cent accuracy is achieved for the near infrared region with wavelengths of 1152 and 1248 nm [7]. Ioos et al. [8] study the influence of the Fusarium and Microdochium nivale moulds and the formation of mycotoxins connected to them on naturally infected grain seed. Fernandez et al. [10] offer near infrared spectroscopy as a quick and cheap method for discovery of the toxic matter alfatoxin B1 (AFB1) in maize and barley. The best predictive model to detect AFB1 in maize is obtained using standard normal variate and detrending (SNVD) as scatter correction. In the case of barley, the best predictive model is developed using SNVD on the dispersive NIRS instrument.

There are already algorithms offered for the discovery of Fusariosis infected maize kernels through analysis of their spectral characteristics on the grounds of their description through linear discrete models of the Autoregression type [2, 3]. On the grounds of the achieved results, an algorithm is offered, which discovers the Fusariosis infected maize kernels through an analysis of the model series and its coefficients. It is established that when the model series is lower than second, then the kernel is healthy, and when the series is higher than fifth, it is typical for diseased kernels. In the case of the fourth series of the model, the detection of the diseased kernels is made on the grounds of А2 and А3 coefficients of the model. As the obtained results concern a small number of kernels, this is a prerequisite for the analysis of a set of maize kernels with bigger volume in order to achieve exact coefficients of the AR model. In [3] the procedure for evaluation of the characteristics of a set of kernels with bigger volume is repeated. It is established that the best series for both classes is the ninth series, but this is not a determining factor for identification of the kernels. That is why the coefficients of the models for the both classes of kernels are analysed. А5 coefficient of the model is used as a criterion for identification, and the other coefficients are commensurable for both classes. The achieved accuracy of identification for healthy and diseased kernels is 70 per cent and 80 per cent, respectively [3].

The purpose of this article is to choose signs and formulate the criteria for identification of Fusariosis infected maize kernels through the introduction of the spectral characteristics of diffuse reflection from the kernels with linear discrete models and the selection of a suitable classification approach. The influence of the kernel variety on the identification accuracy will also be analysed.

Material and Methods

1. General information about the research subjects

The research subject is the pink Fusariosis disease (Fusarium Moniliforme) and its occurrence on maize kernels. Seven varieties of maize kernels were examined – Knezha 308, Knezha 436, Knezha 613, Knezha 620, 26A, XM87/136 and Ruse 424. They have been certified by the Maize Institute in the town of Knezha since 2008. 700 spectral characteristics of diffuse reflection were taken – 350 of healthy and 350 of diseased maize kernels in the range from 456 to 1140.5 nm. The system for obtaining spectral characteristics of diffuse reflection from the maize kernels is presented in [4]. USB4000-VIS-NIR spectrophotometer of the Ocean Optics company was used, as well as QR200-7-VIS-NIR probe for measuring the diffuse reflection form the subject surface. The spectral characteristic of each kernel was obtained for its back side and the germ side, pursuant to the methodology described in [4]. These characteristics show the dependency of the wavelength λ, nm on the intensity of the reflected radiation from the maize kernels Sλ, in absolute values. The achieved database with spectral characteristics is shown in [4].

The taken spectral characteristics, shown on Fig. 1, are normalized through:

,                                                                                           (1)

whereas  is the value of the intensity of the reflected radiation with wavelength ,

is the maximum value of the intensity of the reflected radiation for the n-th spectral characteristic.

а) back side                                                                              b) germ side

variety Knezha 308

а) back side                                                                     b) germ side

variety Knezha 436

Figure 1. Regulated spectral characteristics of two varieties of maize kernels

2. Operation algorithm for division of healthy from Fusariosis infected maize kernels through linear discrete models

The linear discrete model of the Autoregression (AR) type is described through the following equation:

,

where k is the k-th value of the wavelength λ in nm;

are the coefficients of the Autoregression model (AR);

is the intensity of the radiation reflected from the maize kernels for the k-th value of the wavelength λ in nm;

n  is the model series of the Autoregression type;

is the difference (error) between the modelled and the real characteristics.

The algorithm shown on Fig. 2 is offered for the identification of Fusariosis infected maize kernels.

There are numerous methods for formation of training and test sets when there are big databases. In one of the approaches for selection of representative objects, the objects are selected so that they are uniformly distributed over the output database. A well-known representative of this approach is the Kennard and Stone Algorithm. When using it, the desired number of objects to be selected from the output ones is given [9]. The obtained spectral characteristics are distributed into two sets. The training set includes 30 spectres of healthy and 30 spectres of diseased maize kernels of one variety or totally 210 spectres of healthy and 210 spectres of diseased kernels for all the seven varieties. The test set includes 20 spectres of healthy and 20 spectres of diseased maize kernels of one variety or totally 140 spectres of healthy and 140 spectres of diseased kernels for the seven varieties.

Figure 2. Algorithm for identification of healthy and Fusariosis infected maize kernels

The n-th series of the linear discrete model, describing the spectral characteristics of the healthy class and diseased class of kernels, is analysed. The obtained series of the discrete model of the Autoregression (AR) type is presented in Table 1.

The obtained results show that the model series is not a determining indicator for identification of the kernels. Table 1 shows that the 10th series of the model is dominating for the seven varieties of maize kernels. That is why only the 10th series will be used in order to receive the coefficients of the model from the training set. Therefore ten coefficients should be calculated for each variety. Three cases for the A-coefficients of the AR model are obtained and they are shown on Fig. 3.

In the first two cases, the a) and b) group of the healthy kernels is clearly distinguishable from the group of the diseased kernels. In the third case – c) – there is an overlapping of the healthy and diseased kernels.

In order to formulate the identification criterion, the limit value of АLV should be determined between the two classes of kernels – healthy and diseased. To this end, the maximum distance ∆A between the class of the healthy and the class of the diseased maize kernels should be calculated for each of the ten calculated coefficients. The next step is to select the biggest distance from the calculated maximum distances ∆A.

Table 1.                AR model series describing the normalized spectral characteristics of healthy and diseased kernels

| Model series n Corn kernels variety | Back side | Germ side |
| --- | --- | --- |
|  | healthy | diseased | healthy | diseased |
| Knezha 308 | 8 | 6 | 8 | 6 |
| Knezha 436 | 10 | 10 | 8 | 10 |
| Knezha 613 | 8 | 10 | 10 | 8 |
| Knezha 620 | 10 | 10 | 10 | 10 |
| 26 А | 10 | 10 | 8 | 10 |
| ХМ 87/136 | 10 | 10 | 10 | 10 |
| Ruse 424 | 10 | 10 | 10 | 10 |

а)                                                                       b)

c)

Figure 3. Three cases for the A-coefficients of the AR model

The distance ∆A is calculated on the grounds of the three variants of the received A-coefficients from Fig. 3 in the following way:

- - for variant a)

- - for variant b)

- - for variant c)

whereas  and  are the minimum and maximum value, respectively, of the coefficient  for healthy kernels;

and  are the minimum and maximum value of the coefficient  for the diseased kernels.

As there is no clear distinction between the healthy and diseased class in variant c), the mean values  and  of the coefficient  for the both classes of maize kernels should be determined.

The biggest distance from the calculated distances for the ten coefficients is chosen and it corresponds to the А1 coefficient. The limit value of the first coefficient А1LV between the healthy kernels class and the diseased kernels class is determined (shown on Table 2), thus on the grounds of the received coefficient variants, shown on Fig. 3, the conditions for identification of healthy and diseased maize kernels from the test set are formulated (Table 3).

Table 2. Limit values between healthy and diseased maize kernels

| variety | Limit value А1LV for back side | Limit value А1LV for germ side |
| --- | --- | --- |
| Knezha 308 | - 0.2696 | - 0.2788 |
| Knezha 436 | - 0.2168 | - 0.2296 |
| Knezha 613 | - 0.2786 | - 0.2987 |
| Knezha 620 | - 0.3792 | - 0.3915 |
| 26 А | - 0.2895 | - 0.3317 |
| ХМ 87/136 | - 0.2925 | - 0.2743 |
| Ruse 424 | - 0.2812 | - 0.3038 |

Table 3. Conditions for classification of maize kernels through the A-coefficients of linear discrete models

| Variant | Rules | Result |
| --- | --- | --- |
| Variant а) | If A1j > А1LV, then | corn kernel is healthy |
|  | If A1j < А1LV, then | corn kernel is diseased |
| Variant b) | If A1j > А1LV, then | corn kernel is diseased |
|  | If A1j < А1LV, then | corn kernel is healthy |
| Variant c) | If A1j > А1LV, then | corn kernel is healthy |
|  | If A1j < А1LV, then | corn kernel is diseased |

3. Experimental researches

In order to evaluate the accuracy of identification, the test sets of spectral characteristics, determined through the Kennard and Stone method, are used. The spectral characteristics of the healthy and diseased kernels from the test set are taken from the back side and from the germ side.

The calculated coefficients for each spectral characteristic are checked pursuant to the criteria formulated above and after one of the conditions is met, the final result concerning the type of the maize kernel is worked out. The results from the evaluation of the accuracy of identification of maize kernels from the test set through the use of the coefficients of the linear discrete models are shown in Table 4.

Table 4. Results from the verification of the accuracy of identification of maize kernels compared to the test set through A-coefficients of the linear discrete models

| Corn kernels variety | Coefficients variant | Number of correct classified corn kernels | % Correct classified corn kernels | Number of non - classified corn kernels | % non - classified corn kernels |
| --- | --- | --- | --- | --- | --- |
| Knezha 308 | Healthy – back side | c | 12 | 60 | 8 | 40 |
|  | Healthy – germ side | c | 10 | 50 | 10 | 50 |
|  | Diseased - back side | c | 12 | 60 | 8 | 40 |
|  | Diseased - germ side | c | 8 | 40 | 12 | 60 |
| Knezha 436 | Healthy – back side | b | 19 | 95 | 1 | 5 |
|  | Healthy – germ side | b | 19 | 95 | 1 | 5 |
|  | Diseased - back side | b | 20 | 100 | 0 | 0 |
|  | Diseased - germ side | b | 20 | 100 | 0 | 0 |
| Knezha 613 | Healthy – back side | c | 8 | 40 | 12 | 60 |
|  | Healthy – germ side | c | 13 | 65 | 7 | 35 |
|  | Diseased - back side | c | 8 | 40 | 12 | 60 |
|  | Diseased - germ side | c | 12 | 60 | 8 | 40 |
| Knezha 620 | Healthy – back side | c | 16 | 80 | 4 | 20 |
|  | Healthy – germ side | c | 17 | 85 | 3 | 15 |
|  | Diseased - back side | c | 19 | 95 | 1 | 5 |
|  | Diseased - germ side | c | 11 | 55 | 9 | 45 |
| 26 А | Healthy – back side | а | 20 | 100 | 0 | 0 |
|  | Healthy – germ side | а | 18 | 90 | 2 | 10 |
|  | Diseased - back side | а | 20 | 100 | 0 | 0 |
|  | Diseased - germ side | а | 20 | 100 | 0 | 0 |
| ХМ 87/136 | Healthy – back side | а | 20 | 100 | 0 | 0 |
|  | Healthy – germ side | а | 20 | 100 | 0 | 0 |
|  | Diseased - back side | а | 20 | 100 | 0 | 0 |
|  | Diseased - germ side | а | 20 | 100 | 0 | 0 |
| Ruse 424 | Healthy – back side | b | 20 | 100 | 0 | 0 |
|  | Healthy – germ side | b | 20 | 100 | 0 | 0 |
|  | Diseased - back side | b | 19 | 95 | 1 | 5 |
|  | Diseased - germ side | b | 20 | 100 | 0 | 0 |

The obtained results show that the accuracy of identification of diseased kernels of ХМ87/136 variety is 100 per cent. High accuracy of identification is achieved with the following varieties: Ruse 424 (98.75%), Knezha 436 (97.5%) and 26А (97.5%). The percentage of identification for the other three varieties is lower: for Knezha 620 – 78.75%, for Knezha 308 – 52.5% and for Knezha 613 – 51.25%.

CONCLUSION

A classifier of the linear discrete model type could be used for identification of healthy and Fusariosis infected maize kernels for the following varieties: 26А, Knezha 436, ХМ87/136 and Ruse 424.

The accuracy of identification for the Knezha 308, Knezha 613, Knezha 620 varieties is lower. Other classification procedures should also be used for them, in order to obtain higher accuracy of identification.

The obtained results show that the variety influences the identification accuracy.

# REFERENCES

- Damyanov Ch. Non-destructive identification of the quality in food products automatic sorting systems. Academic publisher of the UFT - Plovdiv, 2006.

- Draganova Ts., Pl.Daskalov, R. Tsonev, An algorithm for Fusarium disease maize grains recognition by analyzing the spectral characteristics., Proceedings of University of Rousse “Angel Kanchev", Vol. 40,1.1, 2003, p.33-38.

- Mancheva, V., Pl.Daskalov, R. Tsonev Ts. Draganova. Investigation the Possibility of Modeling the Spectral Data of Sound and Fusarium- damaged Corn Kernels by Linear Discrete Models, Proceedings of the Student Scientific Session, University of Rousse "Angel Kanchev", 2009, p. 46-50.

- Mancheva, V., Pl.Daskalov, R. Tsonev Ts. Draganova. Creation of spectral characteristics database for Fusarium diseased corn seeds recognition, Proceedings of the University of Rousse "Angel Kanchev", Vol. 48, 3.1, 2009, p. 150-157.

- Tomov N., Jordanov J. Maize in Bulgaria., S., Zemizdat, 1984.

- Delwiche S. R. Classification of Scab- and other mold- damaged wheat kernels by near-infrared reflectance spectroscopy, Transactions of the ASAE, 2003, Vol. 46(3): 731–738.

- Delwiche S.R., C.S. Ganes. Wavelenght selection for monochromatic and bichromatic sorting of Fusarium-damaged wheat, Applied Engineering in Agriculture, 2005, Vol. 21(4): 681−688.

- Ioos R., A. Belhadj, M. Menez, A. Faure. The effects of fungicides on Fusarium spp. and Microdochium nivale and their associated trichothecene mycotoxins in French naturally-infected cereal grains, Crop Protection 24 (2005) 894–902.

- Facchin S., J. Trierwieler, V. Conz, Soft sensor design: A new approach for variable selection., 2nd Mercosur Congress on Chemical Engineering.

- V. Fernandez-Ibaсez et al. Application of near infrared spectroscopy for rapid detection of aflatoxin B1 in maize and barley as analytical quality assessment, Food Chemistry 113, 2009, p. 629-634.

Corresponding author: assoc. professor Plamen Daskalov Department of Automatics,information and control engineering, University of Russe, 8 Studentska Street, 7017 Rousse, BULGARIA;  e-mail: daskalov@ru.acad.bg, tel. (082) 888 281

ACKNOWLEDGEMENT

The study was supported by contract № BG051PO001-3.3.04/28, "Support for the scientific staff development in the field of engineering research and innovation”. The project is funded with support from the Operational Program "Human Resources Development" 2007-2013, financed by the European Social Fund of the European Union

# Text boxes

Sλn

Sλn

λ, nm

λ, nm

Sλn

Sλn

λ, nm

diseased

diseased

healthy

healthy

λ, nm

healthy

diseased

diseased

Number of A - coefficients

Number of A - coefficients

А-coefficients

А-coefficients

Number of A - coefficients

А-coefficients