|  | Analysis of the roadworthiness of Fiat Ducato vehicles using Pareto diagrams Emil Savev |
| --- | --- |

Abstract: The article presents results from the research of the reliability of the Fiat Ducato engine and suspension renovated using the Pareto method. Their most common failures and repairs are identified and present in diagram.

Keywords:  reliability, failures, repairs, engine, gearbox, method of Pareto

1.  Introduction

The limitation of the natural resources, increased demands for environmental protection and the complexity of the system design of the modern cars require high reliability during their operation. Successful solution of solving these tasks can be achieved by taking management decisions, based on information obtained from statistical data for the failures occurred, the repair expenses and the unexpected breakdown of the vehicles.

The statistical data can be used to determine the most common failures of the structure, probable causes and ways to minimize them. This kind of tasks can be successfully solved using the Pareto approach, one of the best methods for quality management.

2. Materials and methods

In 1897 Italian economist V. Pareto introduced a formula describing the variability of distributions of wealth. This idea in 1907 was graphically illustrated by a chart from the American economist Max Lorenz. The two scientists showed that most often the largest part of income or wealth does not belong to the large number of people. The famous American expert on quality management Joseph Juran used this method. He applied the Pareto principle to quality issues. This allowed to divide the factors affecting the quality of “the vital few and the useful many”. Generally it turned out that a large number of defects and the

associated losses come from a relatively small number of reasons. J. Zhuang named this approach the Pareto Analysis.

Pareto diagram represents a particular form of vertical bar graph that allows to determine what the problems are and how they can be resolved. The construction of this chart is based on processing of statistical information or other form of data collection. Pareto chart focus on actually the most important factors of the study (the highest bars in the graph) and less to those which are insignificant. Pareto charts for analysis of the reliability (Fig. 1) are built on the following algorithm:

1. Classification of failures chosen in accordance to the studied object.

2. Defining the form for registration of the failures.

3. Developing methodology for processing statistical information.

4. Processed data are arranged in descending order.

5. Plot a horizontal and two vertical axes. On the horizontal axis are plotted the considered factors. On the left vertical are plotted the measured values ​​of the analyzed parameters, and on the right - relative values ​​of this parameter as a percentage of total value.

6. Plot a bar chart for different types of failures.

7. Draw a Pareto curve. On the Intervals corresponding to each vertical of the horizontal axis are plotted the accumulated sums (measured in units or in percentages) which are joined by straight lines.

Fig. 1. Cumulative curve

The aim of the study is to identify and compare the most typical of Fiat Ducato lorry truck. Pareto principle was used as a scientific tool. Based on this principle, an analysis of the cost of repairing various types of failures is made. Csp indicator is used to determine the average specific costs (materials and labor) for distance covered per unit of time.

(1)

Where Cij is the cost of removing the ith type of failure of the jth vehicle;

L – the mileage of jth vehicle run during the study

3.Experimental results

The study was conducted based on statistical data obtained from repair expense reports made to eliminate or prevent failures in different systems of engines and transmissions for 29 cars Fiat Ducato. The total distance covered  is 5134432 km and the average distance is 177049 km. For the engines and transmission of the vehicles 462 failures were registered and divided into 17 classes (groups).

For each group of failures (repairs) of a model Csp costs and their relative share in percentage C% was determined using formula (1) (Table 1).

| № | Type of failure (repair) | Сsp lv/1000 km | C% |
| --- | --- | --- | --- |
| 1. | Front hub bearing replacement | 1.84 | 18.18 |
| 2. | Clutch change | 1.48 | 14.62 |
| 3. | Front strut bearing replacement | 1.31 | 12.94 |
| 4. | Gearbox repair | 1.21 | 11.95 |
| 5 | Joint replacement | 1.07 | 10.53 |
| 6. | Front wishbone bushes replacement | 0.96 | 9.48 |
| 7. | Ball joint replacement | 0,87 | 8,59 |
| 8. | Starter motor repair | 0.45 | 4.45 |
| 9. | Engine rubber mounting change | 0.34 | 3.36 |
| 10. | Bar link replacement | 0.12 | 1.19 |
| 11. | Power steering rack replacement | 1.38 | 0.17 |
| 12. | Thermostat replacement | 0.07 | 0.72 |
| 13. | Welding on the base of the front shock absorber | 0.06 | 0.60 |
| 14. | Inner steering connecting rod replacement | 0.05 | 0.44 |
| 15. | Clutch pump replacement | 0,03 | 0,28 |
| 16. | Alternator replacement | 0.02 | 0.21 |
| 17. | Rear hub bearing replacement | 0.02 | 0.21 |

Table 1

To analyze the reliability during operation of engines and transmissions for the investigated vehicle based on data from Table 1, bar chart and Pareto charts were built (Fig. 2).

Fig. 2. Pareto chart for Fiat Ducato engines and gearboxes

From the Pareto chart (Fig. 1) can be determined that Fiat Ducato includes the following four typical failures (repairs):

- clutch change

- front strut bearing replacement

- joint  replacement

-gear box repair

The frequent changes of elements of the chassis and suspension (bearing, hub bearing, front wishbone bushes, ball joint) is due to the poor country road conditions and the replacement of the original spare parts with alternative, which have less reliability and higher probability for failures.

From the precise analysis of failures in the gearbox can be concluded that the reason for repairs is also the normal wear of gearbox parts (synchronizers, gears, bearings). The defects occur in the range of 150000 km and above.

4.Conclusion

The results of the survey allow detecting the most unreliable components and systems as well as the reasons for their frequent repairs. This could help management staff to take appropriate decisions that improve reliability and increase the efficiency of maintenance of these cars.

5.References

- Кумэ Х., Статистические методы повышения качества: Пер. с англ. / Под ред.. - М.:Финансы и статистика, 1990.

- Netes V.A., Pareto analysis approach to reliability improvement / 2d International Workshop on the Design of Reliable Communication Networks (DRCN 2000). April 9-12, 2000. Munich. Proceedings. Mьnchen: Herbert Utz Verlag, 2000. P. 187-191.

- Исикава К., Японские методы управления качеством: Сокр. пер. с англ. - М.: Экономика, 1988.

| Emil Georgiev Savev1 | PhD Student, , Department Transport, University of Ruse, Ruse, Bulgaria, e-mail: Emil_g.s@abv.bg , tel. +359 82 888 605 |
| --- | --- |

The study was supported by contract № BG051PO001- 3.3.04/28, "Support for the Scientific Staff Development in the Field of Engineering Research and Innovation”. The project is funded with support from the Operational Program "Human Resources Development" 2007-2013, financed by the European Social Fund of the European Union.